# Attachment A: Scope of Work for Services / Technical Specifications

Background

The USAID Cybersecurity for Critical Infrastructure in Ukraine Activity (the Activity) is a program funded by USAID. The overall goal of the Activity is to reduce and potentially eliminate cybersecurity vulnerabilities in Critical Infrastructure (CI), and to transform Ukraine from a compromised, reactive cybersecurity actor to a proactive cybersecurity leader.

Over a four-year period, the Activity will increase resilience and build capacity to prevent, detect, and respond to cyberattacks against CI in Ukraine. To achieve this goal, the Activity is implementing the following components:

Component 1: Strengthening the cybersecurity enabling environment

This component will strengthen the cybersecurity resilience of Ukraine’s CI sectors by addressing legislative gaps, promoting good governance, enabling collaboration between stakeholders, and supporting cybersecurity institutions. This component will also build the technical capacity of key sectors through increased access to cybersecurity technology and equipment.

Component 2: Developing Ukraine’s cybersecurity workforce

This component of the Activity will address workforce gaps through interventions that develop new cybersecurity talent and build the capacity of existing talent. These interventions will address the entire workforce pipeline, the quality of education received by cybersecurity specialists, and industry training programs to rapidly upskill Ukraine’s workforce to respond to immediate cybersecurity vulnerabilities.

Component 3: Building a resilient cybersecurity industry

A growing cybersecurity industry in Ukraine will contribute directly to national security and prosperity. This component will seek to build trust and collaboration between the public and private sector to develop innovative solutions for future cybersecurity challenges; spur investment and growth in the broader cybersecurity market in Ukraine through greater access to financing; support smaller cybersecurity companies to rapidly increase the number of local cybersecurity service providers; and offer mechanisms for Ukrainian firms to connect with industry partners to enable better access to innovations and business opportunities.

- Context

## The State Service for Special Communications and Information Protection (SSSCIP) is a specialized central executive body responsible for ensuring Ukraine’s cybersecurity, development and implementation of the government policy to protect the government information resources and critical information infrastructure. Following the legislation, SSSCIP is responsible for many critical infrastructure protection issues. First of all, it's cyber security. For this purpose, the SSSCIP is developing the capabilities of its particular unit - the State Cyber Protection Center, which carries out practical cyber security measures, provides sensors on CI objects, collects information about cyber incidents, provides assistance to those CI objects which were attacked, provides recovery and related improvement services. Such activities are dependent much on the readiness to assist rapidly, thus use mobile teams (esp. for OT/air gapped infrastructure) with necessary technical capabilities to diagnose systems and quickly assist in recovery and remediation.

- Objectives

## The Activity will support SSSCIP to provide UA30 and CERT-UA teams with cyber security mobile kits (‘fly-away kits’)  to rapidly respond to CI cyber emergencies (especially in the energy sector), perform scheduled maintenance and audit, impact the cybersecurity maturity within CI entities, and increase readiness of CI workforce to respond to cyber incidents. The dedicated technical focus of the mobile kits is on operational technologies (OT), industrial networks and infrastructures (SCADA-related etc).

## The Activity will support SSSCIP, as feasible, with provision of:

## Sensor, audit and incident assessment kits to conduct assessments and related works over IT/OT infrastructures

## Mobile intrusion detection/analysis kits and related technical support to assist CI operators to rapidly detect and respond to attacks

## Disaster recovery kits that collect critical system backups that can be physically isolated in case of ransomware attacks or physical destruction slowing down recovery efforts

## Mobile means to deploy and use equipment at remote locations.

- Tasks:

The Activity is searching for Vendor, who will provide the following services:

- Supply technical equipment (based on the Technical specifications - see Annex A)

- Execute installation of equipment

- Provide trainings for SSSCIP employees (at least 20 participants)

- Deliverables schedule:

| # | Deliverable |
| --- | --- |
| 1 | Provision and delivery of the technical equipment Sub-Deliverables: - equipment supplied - deployment plan agreed |
| 2 | Installation and configuration of equipment Sub-Deliverables: - kits are configured - deployment plan executed |
| 3 | Preparation and training for SSSCIP employees (at least 20 participants) Sub-Deliverables: - staff to be trained selected (within the Recipient personnel) - staff trained |

- TECHNICAL SPECIFICATIONS

(an integral part of the documentation for this RFP- REQ-KYI-22-0173)

| № | Description of the Goods/Services | Quantity | UM |
| --- | --- | --- | --- |
| Sensors - IT |
| 1.1 | Networking |
|  | C9200L-24T-4X-E | Catalyst 9200L 24-port data, 4 x 10G, Network Essentials | 10 | Item |
|  | CON-SNT-C920L24X | SNTC-8X5XNBD Catalyst 9200L 24-port data, 4 x 10G, Ne | 10 | Item |
|  | C9200L-NW-E-24 | C9200L Network Essentials, 24-port license | 10 | Item |
|  | C9200L-24T-4X-E | Europe AC Type A Power Cable | 10 | Item |
|  | CON-SNT-C920L24X | Config 5 Power Supply Blank | 10 | Item |
|  | C9200L-NW-E-24 | Catalyst 9200 Blank Stack Module | 20 | Item |
|  | C9200L-24T-4X-E | C9200L Cisco DNA Essentials, 24-port Term license | 10 | item |
| 1.2 | Sensor computing |
|  | UCS-M6-MLB | UCS M6 RACK, BLADE MLB |  |  |
|  | UCSC-C220-M6S | UCS C220 M6 Rack w/o CPU, mem, drives, 1U wSFF HDD backplane | 10 |  |
|  | CON-SNT-UCSCSC22 | SNTC-8X5XNBD UCS C220 M6 Rack | 10 |  |
|  | UCSC-M-V25-04 | Cisco UCS VIC 1467 quad port 10/25G SFP28 mLOM | 10 |  |
|  | UCSX-TPM-002C | TPM 2.0, TCG, FIPS140-2, CC EAL4+ Certified, for M6 servers | 10 |  |
|  | UCSC-RAID-220M6 | Cisco 12G SAS RAID Controller w/4GB FBWC (16 Drv) w/1U Brkt | 10 |  |
|  | UCSC-PSU1-1050W | Cisco UCS 1050W AC Power Supply for Rack Server Platinum | 20 |  |
|  | UCSC-BZL-C220M5 | C220 M5/M6 Security Bezel | 10 |  |
|  | UCSC-RAIL-M6 | Ball Bearing Rail Kit for C220 & C240 M6 rack servers | 10 |  |
|  | UCS-M2-240GB | 240GB SATA M.2 | 10 |  |
|  | UCS-M2-HWRAID | Cisco Boot optimized M.2 Raid controller | 10 |  |
|  | UCS-CPU-I4314 | Intel 4314 2.4GHz/135W 16C/24MB DDR4 2667MHz | 20 |  |
|  | UCS-MR-X64G2RW | 64GB RDIMM DRx4 3200 (16Gb) | 20 |  |
|  | UCS-SD960G6I1X-EV | 960GB 2.5-inch Enterprise Value 6G SATA SSD | 40 |  |
|  | VMW-VSP-STD-3A | VMware vSphere 7 Std (1 CPU, 32 Core) 3-yr, Support Required | 20 |  |
|  | CON-ISV1-VSXSTD3A | VSphere Standard for 1 CPU; ANNUAL List 3-YR Reqd | 20 |  |
| 1.3 | Sensor routing |
|  | L-DNA-C8000V | Cisco DNA Subscription for Catalyst 8000V | 1 |  |
|  | DNA-P-T1-E-3Y | Cisco DNA Essentials On-Prem Lic 3Y – up to 200M (Aggr, 400M) | 10 |  |
|  | SVS-PDNA-T1-E3Y | Solution Support for SW - DNA Essentials OnPrem Lic, T1, 3Y | 10 |  |
| 1.4 | NG-firewall |
|  | FPR1120-NGFW-K9 | Cisco Firepower 1120 NGFW Appliance, 1U | 10 | Item |
|  | CON-SSSNT-FRP11209 | SOLN SUPP 8X5XNBD Cisco Firepower 1120 NGFW Appliance, 1U | 10 | Item |
|  | FPR1120T-T | Cisco FPR1120 Threat Defense Threat Protection License | 10 | Item |
|  | L-FPR1120T-T-3Y | Cisco FPR1120 Threat Defense Threat Protection 3Y Subs | 10 | Item |
|  | CAB-ACE | AC Power Cord (Europe), C13, CEE 7, 1.5M | 10 | Item |
|  | SF-F1K-TD7.0.1-K9 | Cisco Firepower Threat Defense software v7.0.1 for FPR1000 | 10 | Item |
|  | FPR1K-RM-SSD200- | Cisco Firepower 1K Series 200GB for FPR-1120/1140 | 10 | Item |
|  | FPR1K-RM-ACY-KIT | Cisco Firepower 1K Series Accessory Kit for FPR-1120/1140 | 10 | Item |
|  | FPR1000-ASA | Cisco Firepower 1000 Standard ASA License | 10 | Item |
|  | FPR-LTP-QR-LBL | Cisco Firepower QR Label - Internal Use Only | 10 | Item |
| 1.5 | Modules |
|  | GLC-BX-D | 1000BASE-BX SFP, 1490NM | 5 | Item |
|  | GLC-BX-U | 1000BASE-BX SFP, 1310NM | 5 | Item |
|  | GLC-LH-SMD | 1000BASE-LX/LH SFP transceiver module, MMF/SMF, 1310nm, DOM | 10 | Item |
|  | Сopper patch cords | Patch cord cat. 6, RJ45-RJ45 | 100 | Item |
| 1.6 | Network TAP |
|  | GTP-ATX01 | G-TAP A Series, Always On 10/100/1000M copper TAP, AC Power (US Plug) | 10 | Item |
|  | PBK-GTA03 | Power Brick for G-TAP A Series (AC to DC transformer), EU Plug. Not TAA Compliant. | 20 | Item |
|  | GTP-ASF01 | G-TAP A Series, Always On SFP/SFP+ TAP, AC Power (US Plug) | 10 | Item |
|  | PBK-GTA03 | Power Brick for G-TAP A Series (AC to DC transformer), EU Plug. Not TAA Compliant. | 20 | Item |
|  | SFP-502 | 1 Gig SFP, Multimode 850 | 20 | Item |
|  | SFP-532 | 10 Gig SFP+, Multimode 850nm SR | 20 | Item |
|  | GSS-FYS-BAS-PSS | Initial Gigamon Pass-through Support Type with BASIC Support Level (8-5, M-F/R&R), bought with product or within 1 year of original purchase of product | 10 | Item |
| 1.7 | General SCADA Security |
|  | CV-LICENSE | Cisco Cyber Vision Licenses | 1 | Item |
|  | CV-A-100 | Cyber Vision Advantage License for 100 endpoints | 5 | Item |
|  | SVS-CV | Embedded Support for Cisco Cyber Vision | 1 | Item |
|  | CV-IDS-CNTR | Cyber Vision Center Intrusion Detection License | 5 | Item |
| 1.8 | 19 inch transportation rack |
|  | AR0487-0707 | 4u Amazon Rack (with 870mm deep chassis) | 10 | Item |
|  | AA423 | Extruded aluminium chassis 870mm deep | 10 | Item |
|  | EG3-0887 | Easy Glide System | 10 | Item |
|  | AASP0607/BK | Stowage pouch | 10 | Item |
|  | AAPRV | Pressure Relief Valve | 10 | Item |
|  | AAHI3050 | Humidity Indicator | 10 | Item |
|  | AAHSB/BK | 4 x stainless steel handles | 10 | Item |
|  | AAINT610W/BK | Amazon (interstacker) wheel-board | 10 | Item |
|  | AAPLS/BK | pair of linking straps | 10 | Item |
|  |  | A/V mounts - 16 x 45 shore anti-vibration mounts for payloads upto 70kg, Colour - Olive Drab |  |  |
| Sensor - OT |
| 1.9 | SCADA Security |  |  |  |
|  | 2740S#G5AH | SEL-2740S SDN Switch model 2740S#G5AH | 8 | Item |
|  | NS-100-SEL | Dragos Sensor model NS-100-SEL, Dragos Sensor subscription license, NS-100-SEL – 2 years | 8 | Item |
|  | STS-500-E | Dragos SiteStore model STS-500-E, subscription license, STS-500-E – 2 years | 2 | Item |
|  | Dragos Professional service | Rapid Response Retainer - 240 Hours | 1 | Item |
|  | Training | Dragos Training Credit | 40 | Item |
|  | Service | Dragos service - Remote Deployment & Installation | 2 | Item |
| 1.10 | 19 inch transportation rack |
|  | AR0448-0712 | 4u Amazon Rack (with 480mm deep chassis) | 10 | Item |
|  | AA423 | rack fixings | 10 | Item |
|  | EG3-0448 | Easy Glide System | 10 | Item |
|  | AAW003 | Amazon Wheel Kit | 10 | Item |
|  | AASP0407/BK | Stowage pouch | 10 | Item |
|  | AAPRV | Pressure Relief Valve | 10 | Item |
|  | AAHI3050 | Humidity Indicator | 10 | Item |
|  | AAHSB/BK | stainless steel handles | 10 | Item |
|  | AAAVM458 | A/V mounts - 8 x 45 shore anti-vibration mounts for payloads upto 20kg | 10 | Item |
| Audit - kits |
| 2.1 | HW/SW equipment |
|  | Durabook S14I | DURABOOK S14I Black - Rugged laptop (CPU Core-i3, 8GB RAM, 128 GB SSD, Win 10, RS232) | 5 | item |
|  | Lenovo notebook | ThinkPad X1 Carbon Gen 10 (RAM 32GB,CPU Core-i5, SSD 2TB) | 15 | item |
|  | Tableau TX1 | Tableau Forensic Imager (TX1) | 10 | item |
|  | Ekahau Sidekick | Ekahau Sidekick 2 – 3 year service | 5 | item |
|  | External HDD | External HDD 2,5” 2TB USB 3.0 | 10 | item |
|  | Nessus Pro | Nessus Pro, 256 IPs, 3 years service | 1 | item |
|  | Burpsuite Pro | Burp Suite Professional - 3 years service | 15 | item |
| Incident Response Kits |
| 3.1 | Lenovo notebook | ThinkPad X1 Carbon Gen 10 (RAM 32GB, CPU Core-i5, SSD 2TB) | 15 | item |
| 3.2 | Volcano One - Floating | Annual Subscription License, Maintenance, Support, Upgrades, & Feeds for 1 year; Floating Licenses may be installed on multiple devices; Floating Licenses use a cloud-based license manager and therefore require that all users have Internet connectivity to access the Volexity license manager | 3 | item |
|  | Surge Collect Enterprise Team (Unlimited) Multi- Platform | Annual Subscription License, Maintenance, Support, & Upgrades for 1 year; Supports the collection of memory from specified versions of Windows, macOS and Linux systems; Size: Unlimited use within the community of users – 3 year | 1 | item |
|  | Malware and Memory Forensics Training - Public | Five days of Windows, Mac, and Linux Memory Forensics training | 3 | item |
| 3.3 | KON Boot | LEAD 82 - KON Boot 3 year | 10 | item |
| 3.4 | Nextron Thor | THOR Enterprise Pro Unlimited 3 year (Thor full featured license) | 1 | item |
| 3.5 | Maltego | Maltego Enterprise on-premise (3 users, 3 years) | 1 | Item |
| 3.6 | Maltego service | Maltego advanced training | 1 |  |
| 3.6 | Acronis Data recovery | Backup & Recovery software suite | 5 | Item |
| 3.7 | DomainTools | DomainTools Iris (2500) | 1 | Item |
| 3.8 | JOESandbox | JOESandbox Cloud 250/m (basic) | 1 | Item |
| 3.9 | VirusTotal | VirusTotal basic | 1 | item |
| 3.10 | L-FPR9K-24T-TMC-1Y | Cisco FPR9K SM-24 Threat Defense Threat, Malware, URL 1Y Sub | 2 | Item |
|  | HXDP-M5-E-AD | HyperFlex Data Platform M5 Edge Advantage | 6 | item |
| 3.11 | L-FPR4110T-T-1Y | Cisco FPR4110 Threat Defense Threat Protection 1Y Subs | 2 | Item |
| 3.12 | HXDP-M5-E-AD | HyperFlex Data Platform M5 Edge Advantage | 8 | item |
| Other goods |
| 4 | Backup power system |
| 4.1 | Ecoflow | EcoFlow DELTA Pro | 5 | item |
| 4.2 | Diesel Generator | 4 kWh, Diesel, 1Phase, Electric Start, 4 Whell, with Canopy | 5 | item |